## Slide 1
Snow-Terrain Mobility
Performance Analysis
Traction stability & directional accuracy in low-friction terrain
Sensors: IMU • Wheel encoders • Temperature
Sampling: 20 Hz • Format: CSV • Repo: GitHub
Made by:Mohamed Amine boubker &
Mohamed reda berroho
Notes: [Sources]
- Background image: Unsplash (image URL from search results). https://images.unsplash.com/photo-1483921020237-2ff51e8e4b22 (via turn1image0)
[/Sources]

## Slide 2
Motivation
Snow-Terrain Mobility Performance Analysis
Fall 2025
Why snow is hard for autonomous vehicles
Low friction → wheel spin and unstable traction
Uneven/soft surface → speed estimation errors
Cold temperatures → battery & motor performance drop
Loss of heading accuracy → path deviation and safety risk
Key risks
Traction loss
Slip ↑
Wheel spin / control issues
Direction drift
Yaw drift ↑
Navigation error

## Slide 3
Project Objective & Scope
Snow-Terrain Mobility Performance Analysis
Fall 2025
Goal
Use IMU + wheel encoder data to quantify
(1) traction stability and (2) directional accuracy
in snow-like low-friction conditions.
In scope
Time-series sensor analysis (20 Hz)
KPI computation: slip ratio, heading drift
Visualization & reporting
Out of scope (for now)
Real-time embedded control
Physical field testing & long-duration trials
Hardware redesign / mechanical wear studies

## Slide 4
System & Sensors
Snow-Terrain Mobility Performance Analysis
Fall 2025
Data sources used for mobility monitoring
Vehicle
Low-friction
(snow-like) run
Wheel encoders
Wheel speed
→ slip ratio
IMU (gyro + accel)
Yaw rate
→ heading drift
Temperature sensors
Cold effects
→ constraints
Vehicle speed (reference)
Linear speed
for slip computation

## Slide 5
Data Resources
Snow-Terrain Mobility Performance Analysis
Fall 2025
Dataset characteristics
Time-series sensor logs
Sampling rate: 20 Hz
CSV format, stored in GitHub repo
Runs reflect low-traction (snow-like) conditions
Signals (examples)
Signal
Description
wheel_speed
From encoders (m/s)
vehicle_speed
Reference linear speed (m/s)
gyro_z
Yaw rate (rad/s)
accel_x/y
Acceleration (m/s²)
temperature
Sensor / ambient (°C)

## Slide 6
Key Performance Indicators (KPIs)
Snow-Terrain Mobility Performance Analysis
Fall 2025
We evaluate mobility using two primary KPIs
Slip Ratio
≈ 10%
Target threshold: < 15%
Measures wheel slip by comparing encoder-derived wheel speed
against vehicle linear speed. Higher slip indicates traction loss.
Heading Drift
2.13°
Acceptable: < 5°
Estimated by integrating IMU yaw-rate over time. Drift indicates
accumulated directional error in low-friction motion.

## Slide 7
Methodology
Snow-Terrain Mobility Performance Analysis
Fall 2025
Analysis workflow (Python)
1
Load & inspect
Read CSV logs; validate timestamps and sensor ranges
2
Compute slip
Compare wheel speed vs. linear speed → slip ratio
3
Estimate heading
Integrate gyro yaw-rate → heading change over time
4
Evaluate
Compare KPIs to thresholds; highlight worst-case periods
5
Visualize
Plots for slip, drift, and temperature vs. time

## Slide 8
Results (KPI vs Acceptable Limits)
Snow-Terrain Mobility Performance Analysis
Fall 2025
Measured values are well within predefined limits
% of acceptable limit
100%
75%
50%
25%
0%
67%
Slip ratio
43%
Heading drift
Measured
Limit (100%)
Avg slip ratio
10%
Threshold: 15%
Max heading drift
2.13°
Limit: 5°
Conclusion:
Stable traction and
low drift in simulated
snow conditions.

## Slide 9
Evaluation
Snow-Terrain Mobility Performance Analysis
Fall 2025
What the KPIs indicate
Slip ratio below threshold → wheel traction is generally stable
Heading drift far below limit → navigation remains accurate
Combined → vehicle maintains controllability in low friction
Practical takeaway
A simple sensor-based monitoring pipeline can flag
traction loss (slip) and navigation degradation (drift)
without needing expensive external positioning.
Example: slip stays below limit

## Slide 10
Constraints & Limitations
Snow-Terrain Mobility Performance Analysis
Fall 2025
What can affect accuracy and real-world performance
Cold temperatures: reduced battery output and motor torque
Sensor noise and bias: IMU drift can accumulate over time
Surface friction varies (ice vs packed snow vs powder)
Simulation-based analysis: does not capture wind, wear, misalignment
Mitigation ideas (future)
• Bias correction / filtering for IMU
• Wheel slip-aware speed estimation
• Adaptive traction control (closed-loop)
• Field data collection for validation

## Slide 11
Cloud Deployment (AWS EC2)
Snow-Terrain Mobility Performance Analysis
Fall 2025
Minimum deployment: host a small dashboard to view KPIs remotely
Launch a Free Tier EC2 instance (Linux)
Open inbound ports: SSH (22) + Streamlit (8501)
SSH into instance and install Python + requirements
Run: streamlit run dashboard.py --server.address 0.0.0.0 --server.port 8501
Access in browser: http://<EC2-PUBLIC-IP>:8501
Architecture
Browser
Student / instructor
AWS EC2
Streamlit dashboard
(port 8501)
CSV data
Uploaded logs
(or pulled from GitHub)
Notes: [Sources]
- AWS EC2: Connect using SSH. https://docs.aws.amazon.com/AWSEC2/latest/UserGuide/connect-linux-inst-ssh.html
- AWS VPC: Configure security group inbound rules. https://docs.aws.amazon.com/vpc/latest/userguide/working-with-security-group-rules.html
- AWS EC2 Free Tier usage guidance. https://docs.aws.amazon.com/AWSEC2/latest/UserGuide/ec2-free-tier-usage.html
- Streamlit remote deployment troubleshooting / configuration notes. https://docs.streamlit.io/knowledge-base/deploy/remote-start
[/Sources]

## Slide 12
Conclusion & Future Work
Snow-Terrain Mobility Performance Analysis
Fall 2025
Summary
Sensor-based monitoring effectively quantifies snow mobility
Vehicle met targets for traction (slip) and direction (drift)
KPIs provide a clear way to compare runs and detect issues
Next steps
Collect real-world snow data for validation
Add adaptive traction control (closed-loop)
Improve drift estimation with filtering / bias correction
Expand dashboard: run selection, KPI trends, alerts
Thank you!
For listening